## Slide 1
AQUAMONITOR
IoT-Based Smart Water Tank Automation System
Automated pump control, non-contact level sensing, and real-time dashboard telemetry.
ST. XAVIER'S COLLEGE (AUTONOMOUS), AHMEDABAD
Department of Computer Science • Semester 3 IoT Project
Tanvi Patel
Roll: 25AI056
Part I: Context
Barot Yaksh
Roll: 25AI002
Part II: Flow
Nayan Barot
Roll: 25AI027
Part III: Outcomes
[ INSERT SYSTEM VISUAL HERE ] Click to add your circuit image, hardware mockup, or UI dashboard screenshot.

## Slide 2
PART I: INTRO & CONTEXT
The Core Water Management Challenge
THE PROBLEM
Manual monitoring is highly inefficient, leading to resource waste and pump failures.
Key Consequence:
Inductive load spikes and motor burned coil stators.
01 | CRITICAL OVERFLOW WATER WASTAGE
• Manual tracking leads to regular tank overflows.
• Results in hundreds of liters of clean water lost daily.
02 | PUMP DRY-RUN MOTOR DAMAGE
• Pumps run without liquid when source reservoir is empty.
• Causes motor overheating and stator coil burnout.
03 | HIGH ELECTRICITY UTILITY BILLS
• Over-pumping consumes heavy electrical current.
• Inflates monthly household and commercial utility bills.

## Slide 3
PART I: INTRO & CONTEXT
The AquaMonitor Solution
01 | AUTOMATED CONTROL LOOP
• Microcontroller handles starting/stopping parameters automatically.
• Starts pump at <20% and stops it at >90% water level.
02 | PRECISION ULTRASONIC RANGING
• Emits ultrasonic sound waves to compute exact water depth.
• Maintains high-precision measurements within ±1 cm accuracy.
03 | REAL-TIME WEB TELEMETRY
• Pushes metrics instantly to web dashboard using Socket.io.
• Sends mobile browser push notifications during warning states.
THE GOAL
Shifting from human tracking to hardware automation creates a zero-waste water grid.
Primary Benefits:
Prevents overflows, protects motors, and cuts energy bills.

## Slide 4
PART I: INTRO & CONTEXT
Hardware Stack & Architecture
CORE MICROPROCESSOR
NodeMCU ESP8266
Processes sensor signals, runs the control logic, and transmits wireless telemetry packet updates.
✔ Low-power 32-bit CPU core
✔ Onboard 802.11 b/g/n Wi-Fi module
✔ GPIO pins connect sensors & relay
ULTRASONIC SENSOR
HC-SR04 Module
Measures echo return time-of-flight from container top to track exact water depth without liquid contact.
✔ Non-contact ranging (2cm - 400cm)
✔ High resolution (within ±3mm accuracy)
✔ Humidity-safe design prevents rust
ACTUATORS & ALERT
Relay, Buzzer & Pump
Handles high-power switching and sounds physical boundary alarms during empty or overflow thresholds.
✔ 5V Relay for pump circuit control
✔ Active buzzer sounds local alarms
✔ 5V submersible pump simulation

## Slide 5
PART II: METHODOLOGY & METRICS
Operational Flow & Circuit Integration
SYSTEM FLOW
01 | PING RANGE
Sensor sends 10µs sound wave pulse to calculate time delay.
02 | CALCULATE LEVEL
ESP8266 converts travel delay to exact level percentage.
03 | AUTO CONTROL
Relay turns pump ON at <20% and OFF at >90% thresholds.
04 | STREAM DATA
NodeMCU posts HTTP JSON packets to backend API every 3s.
[ INSERT CIRCUIT DIAGRAM / SCHEMATIC HERE ] Click to add your circuit wiring schematic or system block diagram.
Figure: Microcontroller-sensor integration loop showing active ultrasonic echo ranging and automatic wireless telemetry sync.

## Slide 6
PART II: METHODOLOGY & METRICS
Software Architecture & Live Portal
THE SOFTWARE STACK
✔ Node.js & Express: Host local REST API routes to receive sensor data and store history in memory.
✔ Socket.io (WebSockets): Establish bidirectional channels for real-time dashboard updates without page reloads.
✔ Web Push API: Triggers native mobile notifications when system registers empty/overflow limits.
PORTAL FEATURES & UTILITIES
✔ Dynamic Level Tracker: Visual liquid progress bar changes color based on current depth percentage.
✔ Dual Operation Modes: Switch between automated sensor loops and manual relay control toggles.
✔ Configurable Parameters: Input forms allow users to update start/stop threshold parameters on the fly.

## Slide 7
PART III: RESULTS & CONCLUSIONS
Real-World Performance & Utility
🏠 Home Automation
Domestic Settings
Runs overhead and underground refills automatically, saving overhead tank waste, power, and physical inspection.
CORE VALUE:
100% Manual Effort Eliminated
🌱 Crop Irrigation
Smart Agriculture
Maintains optimal reservoir levels for drip lines or drinking pools in the background without crop soil stress.
CORE VALUE:
Automated Moisture Protection
🏭 Facility Safety
Asset Protection
Tracks liquid limits in clinics, blocks, and factories. Protects pump investments from dry-run coil burnout.
CORE VALUE:
Prevents Dry-Run Pump Damage

## Slide 8
PART III: RESULTS & CONCLUSIONS
Conclusion & Project Outcomes
✔ Reliable Ultrasonic Depth Tracking
• Stable distance calculations within a precise ±1 cm window.
• Humidity-proof, non-contact design avoids system rust.
✔ Automated Resource Optimization
• Microcontroller logic completely eliminates manual oversight.
• Ends overflow water waste and limits pump runs.
✔ Extremely Low Prototype Budget
• Full prototype built under ₹1,100 ($14 USD) hardware cost.
• Uses budget-friendly NodeMCU board and HC-SR04.
✔ Highly Scalable Network Design
• Clean local Node.js APIs map sensor data packets easily.
• Ready to link multiple tank nodes across commercial complexes.

## Slide 9
VIVA Q&A SESSION
Questions & Discussion
Presented by: Tanvi, Yaksh, and Nayan (St. Xavier's College)
Discussion Topics: Non-Contact Ultrasonic Precision • Local Loop Hardware Fail-safes API Database Telemetry • Relay Automation Thresholds • Dry-Run Safety Control

## Slide 10
THANK YOU!
Open for Questions & Discussion
PROJECT REPRESENTATIVES
Tanvi Patel
Roll: 25AI056
Part I: Context
Barot Yaksh
Roll: 25AI002
Part II: Flow
Nayan Barot
Roll: 25AI027
Part III: Outcomes